SECTION 10 19 00

DISPOSABLE CUBICLE CURTAINS

PART 1 – GENERAL

  - RELATED DOCUMENTS

- Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

  - SUMMARY

- This section includes the following:

- Cubicle curtains

1.03	PERFORMANCE REQUIREMENTS

- Curtains:  Provide curtain fabrics with the following characteristics:

- Flame retardant, meeting NFPA 701 standards

- Fabricated of polypropylene

- Manufactured with standard nylon mesh or integral (punched) mesh

- Biodegradable

- Disposable

  - SUBMITTALS

- Product Data: Submit copies of manufacturer’s detailed technical data for materials, fabrication, and physical appearance.

- Shop Drawings: Show layout and types of cubicle curtains, sizes of curtains, and number of carriers.

- Samples for Verification: Provide samples of the following:

- Curtain Fabric:  12-inch square swatch or larger sample as required to show complete pattern repeat, from dye lot used for the work, with specified treatments applied.

- Cubicle Schedule:  Use same room designations as indicated on drawings

- Maintenance Data:  Provide fabric manufacturer’s standard maintenance procedure documentation.

  - PROJECT CONDITIONS

- Environmental Limitations:  Do not install cubicles until spaces are enclosed and weatherproof, wet work in spaces is complete and dry, work above ceilings is complete, and ambient temperature and humidity conditions are maintained at the levels indicated for Project when occupied for its intended use.

- Field Measurements:  Where cubicles are indicated to fit to other construction, verify dimensions of other construction by field measurements before fabrication and indicate measurements on Shop Drawings.  Coordinate fabrication schedule with construction progress to avoid delaying the work.

  - WARRANTY

- Provide copy of manufacturer’s standard warranty.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

- Subject to compliance with the requirements listed, provide cubicle curtains from the following manufacturer:

- CS Cubicle Curtains, a Division of Construction Specialties, Inc.

3 Werner Way

Lebanon, NJ 08833

P: (908) 849-4000 / F: (908) 849-4398

CCInfo@c-sgroup.com

www.c-sgroup.com

- Alternative manufacturers will not be accepted

2.02	MATERIALS

- Cubicle Curtain:
<**Note to specifier – please choose the type of disposable curtain being used – Traditional [OR] On The Right Track. Delete option not chosen>

- Traditional Cubicle Curtain [or] On The Right Track

- Fabric:  Provide 100% polypropylene, disposable fabric

2.03	PATTERN AND COLOR

- Cubicle Curtain Fabric: fabric to be of one of the following solid colors:

<**Note to specifier – please choose the desired color or pattern to be used>

- Blue (*only for traditional curtains)

- Green (*only for traditional curtains)

- Beige (*both traditional and On The Right Track)

- Light Blue (*both traditional and On The Right Track)

- Boxed Leaf Pattern (*only for On The Right Track)

- Ivy Pattern (*only for On The Right Track)

2.04	FABRICATION

- Disposable Cubicle Curtain with the following characteristics :

<**Note to specifier – please choose the type of disposable curtain being used – Option 1 Traditional Curtains [OR] Option 2 On The Right Track Curtains.  Delete option not chosen>

- Traditional Curtains:

  - Width:  Equal to track length from which curtain is hung plus 10 percent, but not less than 12" (300 mm).

  - Length:  Equal to floor-to-ceiling height minus 2" from finished ceiling at top and 12” or 15” above finished floor <**Note to specifier – please select either 12” or 15”>

[OR]

- On The Right Track Curtains:

  - Panel size: 69 inches wide by 92 inches high including 19 inches of mesh, hemmed as required.

  - Curtain Loading Tool: Manufacturer’s standard loading tool, The Grabber

  - Curtain Ring Color:

    - Cream

PART 3 – EXECUTION

3.01	EXAMINATION

- Examine areas and conditions in which the cubicle track system will be installed

1. Complete all finishing operations, including painting, before beginning installation of cubicle tracking system materials.

- Verify that surfaces and above ceiling supports are ready to receive work.

3.02	INSTALLATION

- General: Locate the cubicle track as indicated on the approved detail drawing for the appropriate substrate

- Installation of Cubicle Track System:

  - Install cubicle track, secure, rigid, and true to ceiling line.

  - Slide carriers onto the track.

  - Install end cap or stop device.

  - Secure or suspend track to ceiling system. Install with mechanical fasteners or T-Grid clips.

  - Install curtains on carriers ensuring smooth operation.

END OF SECTION

# Text boxes

CS Cubicle Curtains