SECTION 10 21 23

CUBICLE CURTAINS AND TRACKS

PART 1 - GENERAL

1.01	SUMMARY

A.	Provide cubicle curtains and tracks for the following applications.

1.	Hospital bed cubicles.

2.	Examination areas.

3.	Emergency areas.

4.	Dressing areas.

B.	Provide shower curtains at tubs and showers.

C.	Related Work:

1.	Section 09 21 16 - Gypsum Board Assemblies, for wallboard ceilings.

2.	Section 09 51 00 - Acoustical Ceilings, for acoustical ceiling panels.

1.02	SUBMITTALS

A.	Product Data:  Submit manufacturer's product data, installation and maintenance instructions.

B.	Verification Samples:  Submit representative of curtain fabric specified to verify style and color.

C.	Shop Drawings:  Submit reflected ceiling plans indicating locations of cubicle curtain and tracks.

1.03	QUALITY ASSURANCE

A.	Flammability:  Curtains shall pass NFPA 701 - Standard Methods of Fire Tests for Flame Propagation of Textiles and Films.

B.	Mock-Ups:  Install one complete unit for approval prior to installation of remaining cubicle curtains and tracks.  Approved mock-ups may remain in place.

1.04	DELIVERY, STORAGE, AND HANDLING

- Deliver materials and products in unopened factory labeled packages. Store and handle in strict compliance with manufacturer's instructions and recommendations.

PART 2 – PRODUCTS

2.01	MANUFACTURER

- Subject to compliance with the requirements listed, provide cubicle curtains from the following manufacturer:

- C/S Cubicle Curtains, a Division of Construction Specialties, Inc.

3 Werner Way

Lebanon, NJ 08833

P: (908) 849-4000 / F: (908) 849-4398

CCInfo@c-sgroup.com

www.c-sgroup.com

2.02	MATERIALS

- Curtain Tracks:

  - Provide On the Right Track, Inc. cubicle curtain and track system as manufactured by C/S Cubicle Curtains with the following characteristics:

- Surface Mounted Track:  Extruded aluminum with powder coated white finish.

- Dimensions:  1 ½ inches (39 mm) high by 3/8 inch (10 mm) wide.

- Provide straight and bent sections as indicated on drawings

- Track Accessories:  Splices, connectors, hangers, anchors and mounting plates as required

- Loading Zone:  Provide (1) loading zone per track layout to be used as an area for on-loading and off-loading cubicle curtains.

- Curtain Loading Tool:  Provide manufacturer’s standard loading tool, The Grabber.  Provide at minimum 1 Grabber Bar per floor.

- Cubicle Curtains:

  - As fabricated by C/S Cubicle Curtains. Curtains to be custom made from flame-retardant, hospital quality material with a 1 ½" triple hem, including turned edges and a row of stitches at top and bottom of hem, complete with label. Curtains to be fabricated with nylon mesh tops designed for attachment to track without separate hooks.

- Pattern & Color:

<**Note to specifier – please choose either option, a. (used when you have a specific designer pattern you would like to use), OR option b. (used when a C/S standard pattern & color is desired)

  - Cubicle Curtain Fabric: Designer fabric pattern and color to be the following:

- <insert designer fabric pattern & color>

  - Cubicle Curtain Fabric: Select solid or patterned fabric from manufacturer’s standard selection as follows:

- Pattern: RX7004 / Color: <insert color>

- Pattern: Twig / Color: <insert color>

- Pattern: Sugar Lash / Color: <insert color>

- Pattern: Fluent / Color: <insert color>

- Pattern: Flora / Color: <insert color>

- Pattern: Kriya / Color: <insert color>

- Pattern: Flourish / Color: <insert color>

- Pattern: Increment / Color: <insert color>

- Pattern: Moderate / Color: <insert color>

- Pattern: Lynx / Color: <insert color>

- Pattern: Orbit / Color: <insert color>

- Pattern: River Birch / Color: <insert color>

- Pattern: New Shadow Cube / Color: <insert color>

- Pattern: Windsor / Color: <insert color>

- Pattern: Connections / Color: <insert color>

- Pattern: Xanadu / Color: <insert color>

- Pattern: Allegro / Color: <insert color>

- Pattern: Oxford / Color: <insert color>

- Antimicrobial Treatment: <**Note to specifier – please delete this section if antimicrobial and/or liquid resistant treatment is not required>

  - Standard antimicrobial treatment applied to the selected cubicle curtain fabric 
[OR]

  - Nanotex + BioAM spill & stain resistant treatment combined with an antimicrobial agent for protection of fabrics within healthcare settings.

2.03	FABRICATION

- Vertical Curtain Seams: Shall be double needle interlocked.

- Label: Shall be sewn into the top hem of each curtain to identify the width of curtain.

- Mesh Tops: Flameproof nylon mesh, mesh must have ½" spacing as per NFPA requirements. Mesh is to be completely bound with same fabric as the body of the curtain. Mesh to be 19” high at top of curtains.

- Curtains to finish
<**Note to specifier – please choose either 12” or 15”

  - <12”> OR <15”> above the finished floor.

- Panel Size:  
<**Note to specifier – please choose 1 of the following options (a or b)>

  - 69 inches wide by 92 inches high including 19 inches of mesh, hemmed as required.

PART 3 - EXECUTION

3.01	INSTALLATION

A.	Installation of Cubicle Curtains and Tracks:  Install in accordance with manufacturer’s recommendations, including the following:

1.	Verify that ceilings are suitable for installation prior to installation.

2.	Mechanically attach tracks using manufacturer’s recommended anchors and attachment devices.

3.	Install accessories and curtains and test for proper operation.  Replace damaged units.

END OF SECTION

# Text boxes

C/S Cubicle Curtains