SECTION 10 21 24

SURFACE MOUNTED NARROWLINE CUBICLE TRACK AND CARRIERS

PART 1 – GENERAL

  - SUMMARY

- Section includes:

  - Ceiling mounted curtain track

  - Track accessories and attachments

  - SUBMITTALS

- Product Data: Manufacturer’s product data sheets for all specified curtain track.

- Detail Drawings: Mounting details with the appropriate fasteners for specified project substrates.

- Samples: Verification samples of cubicle track, 4" (102mm) in length.  Complete with (1) carrier as specified and stop.

- Manufacturer’s standard installation instructions

  - DELIVERY, STORAGE, AND HANDLING

- Deliver materials in unopened factory packaging.

- Inspect material on delivery to verify products are as specified.

  - WARRANTY

- Manufacturer’s standard warranty against manufacturer defects.

PART 2 - PRODUCTS

  - ACCEPTABLE MANUFACTURERS

- Subject to compliance with the requirements listed, provide cubicle track and carriers from the following manufacturer:

- C/S Cubicle Curtains, a Division of Construction Specialties, Inc.

3 Werner Way

Lebanon, NJ 08833

P: (908) 849-4000 / F: (908) 849-4398

CCInfo@c-sgroup.com

www.c-sgroup.com

- Substitutions: Alternative manufacturers will not be accepted

  - CUBICLE TRACK SYSTEM

- Cubicle Tracks: C/S Cubicle Curtains #NL6062 Narrowline surface-mounted tracks of heavy extruded aluminum alloy 6063-T5, 29/32" x 11/16", slotted to receive roller carriers, complete with accessories and components required for complete and secure installations including splices, end caps and corner bends.

  - Corner Bends:  Corner bends up to 36” radius are to be fabricated in one continuous “L” shape.  Radiuses above 36” to be continuous or spliced based on room condition.

    - Finish:

      - Anodized aluminum

      - White powder coat

- Carriers:

  - C/S Cubicle Curtains NL1062, virgin nylon axle with nylon wheels complete with nickel-plated brass, and aluminum hook assembly.

    - Provide one carrier for each 6" of cubicle curtain width.

END OF SECTION

# Text boxes

C/S Cubicle Curtains